The MAC address is 00-11-11-1A-5F-BD

The instructions to log on are:

1) Switch ON the PC (in the front), and the electronics (the switch is in the back of the rack)

2) Choose Windowx XP mode (the linux doesn't work)

3) Make Ctrl+Alt+Del if asked.

4) Fill the data User/Password/Domain (bllhc_01/Geneva23/ABPC10826).

There is a label with this data on the PC front. If you put other     data, the PC couldn't log on.

5) Validate with OK.

After this, the desktop appears. There is a document (Readme.doc which explains in a short way how to use the program)

To run the application:

1) Click the icon TEST BL LHC placed on the desktop

2) This icon opens the LabView program (VI) and the associated LabView libraries. If during the charge of the VI some warning appears, doesn't matter, just don't make attention.

3) Connect the analog inputs (BNC connectors in the back) and the High Voltage (Red cable in the back) to the detectors.

4) Choose the settings for the acquisition (Integration Time, Gain, Maximun HV, HV Step, Comments, etc) and validate (normally an V appears on the high left side of the labview screen)

5) Run the Program pushing the arrow on the left side of the LabView screen)

6) The VI starts to acquire. When the acqusition is finish, the Red  LED pass to Green. It means that the sofware is generating the output file.

When finished, the VI asks for the folder and name for the file. It is recommended to store it in the folder BL LHC DATA (Desktop) with a .txt extension.

7) The data inside the file appears in columns following the input order (in0 to in12).