07 August 2007

# List of tasks and occupation time of the vacuum stand

# (SEM)

# Description of Equipment

| Equipment | Description |
| --- | --- |
| Vacuum stand for 18-36 SEM | Designed and constructed by IHEP; only 18 SEMs produced at the same time |
| Pump station | Station on base TMP 56 l/s supplied by CERN |
| Pump station | Station on base TMP 170 l/s supplied by CERN |
| Ion pump | Ion pump 100 l/s supplied by IHEP |
| Leak detector | PhoeniXL300 supplied by CERN |
| Gas analyzer | Prizma QMS200F2 supplied by CERN |
| Pressure gauge controller | MaxiGauge TPG256A supplied by CERN |
| Temperature regulater | TR on 24 channels supplied by CERN |
| Date Acquisition unit | Agilent 34970A supplied by CERN |
| Heating container | Container use for heating SEM |

- Preparation procedure

  - Make dry cycles to establish the pressure and gas composition of the manifold itself at different cycle steps.

# № (1 (3)   -   4 hours

- Installation of the SEM on the stand.

- Remove the rest of the copper tubes from the “Sagana” connectors ; cut off the  cooper tubes for release of  the nuts.

- Write  the numbers of the SEM into the data base (Dbase-vac).

- Wash the Sagana inserts rings with alcohol; put in nuts with inserts on the SEM cooper tubes.

- Introduce the SEM copper tubes in the stand “Sagana” connectors and fix ones tightly.

- Fix the 18 thermocouple with a wire on the SEM and connect 12 of the couples to the temperature regulation unit.

- Switch on the vacuum pump station and pump stand with all SEM.

- Leakage test of welds and removable connections of SEM using the procedure of helium overpressure.

- Put the heating containers on SEM’s and tighten with the top covers.

- -Connect the He supply tubes to the heating containers (for 9 containers).

- Pump out the air from 9 containers and fill with He up to a pressure of somewhat higher   than atmospheric.

- Control the tightness by observing the He leak rate during of 3 min: in case of the leak detection, close successively the valves of the SEM for determine the leaking SEM.

- For each of the next 9 containers apply the same procedure (Leak test is execute with help leak detector).

# Leaks of more than 1E-10 l mbar/s are not allowed.

- Preparation of the heating.

- Disconnect the He supply tubes from the containers;

- Dismount the covers of the containers and remove the rubber o-rings from the covers,

- The valve of gas analyser must be closed,

- Heat-insulate all the SEM valves.

4.  Heating. Leakage test of the welds and the removable connections of the SEM

after heating and activation, elimination of possible leaks.

- Start the stand and SEM heating from 200 C to 2200 C and 50 C/hour with help programmator of TR (4 hours). (The pressure not must be more than 1E-4mbar)

- Temperature is kept at  2200 C  (12 hours) with help TR;

# Cool-down stand to 1500 C (1 hour) and this temperature is kept during SEM activation. The SEM temperature is kept 2200 C during cooling stand.

- Input He successively to the each heating container for control tightness of the SEM with help leak detector (2 hours).

- Degassing of RGA and gages, and manual operation of valves (release of gas).

# Start the NEG activation (The start pressure not must be more than 1E-6mbar), the SEM temperature is increase from 2200 C to 3500 C, (500 C/h) (2.6 hours), time activation is 14 hours.

# Slowly open gas analyzer head valve and switch on gas analyzer (record spectrum).

# Degas ion pump (flash)?

# Switch on the ion pump and switch off the pump station.

# Cool-down SEM to 3000 C and is kept about 2 hours (2 hours). Why?

# Cool-down stand to TR0 C. Why?

# Cool-down SEM to 2500 C and is kept about 2 hours (2.4 hours).

# Cool-down SEM to 2000 C (1 hour). Why?

# Record spectrum.

# Switch off gas analyzer and close gas analyzer head valve.

# Dismounting of SEM.

# At the temperature of SEM about 2000 C and pressure <1E-9 mbar close all SEM valves.

# Dismount heating containers.

# open valve for each SEM 2 seconds and observe if pressure increases (check if CH4 is accumulated during cool down)

# Pinch of all SEMs.

- Open all SEM valves and verify the tightness of the cut-off copper tubes which remained on the vacuum stand. (The tightness on the stand side gives a good indication of the tightness of the SEM side of the pinch-off).

- Close ion pump valve and switch of ion pump.

# Cover  the sharp rest of the SEM copper tube with polyamid lacquer.