## Slide 1
10 June 2008
Assessment of BLM thresholds at cold magnets
Agnieszka Priebe, Mariusz Sapinski
CERN
Accelerator and Beams Department
Beam Instrumentation Group
Beam Loss Monitoring Section

## Slide 2: Contents
A.Priebe, M.Sapinski
10 June 2008
2
Introduction and strategy
Main Quadrupole Geometry in Geant4
Loss locations
Energy density in coils
BLM signal
Initial quench level studies
Summary and further development

## Slide 3: Introduction and strategy
A.Priebe, M.Sapinski
10 June 2008
3
Response function
Threshold
ROOT data analysis
Energy deposition
in coils
BLM signal
Fluence
Critical number
of protons
Geometry and material description
LHC Design Report
LHC Layouts
edms
Magnetic field
ROXIE
Geant4 simulations
Quench level
Loss maps
Difficult to find the data!

## Slide 4: Main Quadrupole Geometry
10 June 2008
4
A.Priebe, M.Sapinski
MQ

## Slide 5: Superconducting Coils
A.Priebe, M.Sapinski
10 June 2008
5
Coil simplifications:
Cu wedges
An angle (displacement respectively to a centre of a coil-creating circle)
Endings
Weighted density ρ: 7.7801 g/cm3
Copper to superconductor ratio: 1.95 ± 0.05
Magnetic field map

## Slide 6: Read-out geometry
A.Priebe, M.Sapinski
10 June 2008
6
r = 2
r = 1
r = 0
Division in z
Division in φ
Division in r
Δz = 0, 1, …, 299 →10.53 mm
Δφ = 0, 1, …, 89 →4 °
Δr = 0, 1, 2 →5.12 mm
[mJ/cm3]
2D histogram: (φ, r) weighted by energy density
bin size << shower scale
→ binning is correct
THE BASIC CELL
Distortion due to B

## Slide 7: BLMs
A.Priebe, M.Sapiński
10 June 2008
7
Real situation:
BLM: ø = 87 mm, l = 491 mm
Geant4 simulation:
Plate: a = 5 mm, b = 90 mm, l = lsector
Reasons of use this kind of detector geometry:
Flexibility (different BLM positions on various magnets)
Comparison with previous simulations
Scoring particles

## Slide 8: Loss locations
MO
MQ
BPM
loss 1
loss 2
loss 8
loss 3
loss 4
loss 5
loss 6
loss 7
A.Priebe, M.Sapinski
10 June 2008
8
Beam pipe
BPM
Beam screen
Beam pipe and
Cross - section
Particle: p+
Energy: 7 TeV
Angle: 240 μrad
Time: 30min/p+
→ use lsf
→ try GRID

## Slide 9: ρEdep in the coil & BLM signal
A.Priebe, M.Sapinski
10 June 2008
9
ParticleGun: (119.69; 80; -2360 ) 1020 events
Particle number peak ~ 1m after the beam loss → 1st BLM was located correctly !
He-Vessel
MQ Coil
Beam Screen
Beam Pipe
Particle Gun
Virtual Interconnection Plane
BLM1
BLM2
MO
BPM
Loss8
L.Ponce „Positioning of the LHC BLM”
Geant3
Geant4
Critical number of protons
≈ 9 · 107
Quench level = 1.41 mJ/cm3

## Slide 10: BLM signal
10 June 2008
10
Angular Distribution (in BLM1)
Number of protons
Mean: 1.345
LHC response function 60° (M.Stockner)
≈ 77°
A.Priebe, M.Sapinski
R.f. 60°
7 TeV total signal: 2.2 aC/p
R.f. 90°
7 TeV total signal: 2.0 aC/p
Spectrum of secondary particles
arccos(pz/ptot) [rad]
Signal folding with the response function

## Slide 11: Note 44 vs. Geant4 simulation
10 June 2008
11
A.Priebe, M.Sapinski
r Coil = 0
Coil
LHC Project Report 44 (CASIM simulations)
„Quench levels and transient beam losses in LHC magnets”
J.B.Jeanneret, D.Leroy, L.Oberli, T.Trenkler
1996
Results from Geant4 simulation
ED = p0 · ( r – p1) p2
r Coil = 1
r Coil = 2

## Slide 12: Summary and further aims
FURTHER DEVLOPMENTS
Investigations of SSS geometry variations on threshold.
Development of C9R7 (Dispersion Suppressor) region.
Q6 in IP3 (large expected losses).
SUMMARY
Complex magnet geometry has been implemented in Geant4.
Preliminary threshold for the first BLM on Short Straight Section is about 7.7 ·10 -5Gy (fast losses).
Comparison with Geant3 simulations – good agreement.
Comparison with CASIM – similar results.
10 June 2008
12
A.Priebe, M.Sapinski

## Slide 13
10 June 2008
Thank you for your attention !!!
A.Priebe, M.Sapinski
13

## Slide 14: Comparison with Geant3
10 June 2008
14
A.Priebe, M.Sapinski
L.Ponce „Positioning of the LHC Beam Loss Monitors”

## Slide 15: ρEdep in the coil & BLM signal
A.Priebe, M.Sapinski
10 June 2008
15
ParticleGun: (119.19; 80; -1000 ) 640 events
BLM peak ~ 60 cm after the beam loss
He-Vessel
MQ Coil
Beam Screen
Beam Pipe
Particle Gun
Virtual Interconnection Plane
BLM1
BLM2
MO
BPM
Loss5
L.Ponce „Positioning of the LHC BLM”
Geant3
Geant4

## Slide 16: Problems & impediments
10 June 2008
16
A.Priebe, M.Sapinski

## Slide 17: Problems & impediments
10 June 2008
17
A.Priebe, M.Sapinski

## Slide 18: Problems & impediments
10 June 2008
18
A.Priebe, M.Sapinski

## Slide 19: Problems & impediments
10 June 2008
19
A.Priebe, M.Sapinski

## Slide 20: Cell volume
A.Priebe, M.Sapinski
10 June 2008
20
r = 0, 1, 2
ρ = 0, 1, …, 90
z = 0, 1, …, 300
rCoil,inner = 28 mm
rCoil,outer = 43.36 mm
rCell,inner = 28 + r · (rCoil,outer-rCoil,inner) · ⅓
rCell,outer = 28 + (r+1) · (rCoil,outer-rCoil,inner) · ⅓
V = π · [(rCell,outer)2 - (rCell,inner)2] · z ·⅟300 ·⅟90

## Slide 21: Energy depositions in the coil
A.Priebe, M.Sapinski
10 June 2008
21
2D histogram: (φ, r) weighted by energy density
Log (z)
Log (z)
[mJ/cm3]
[mJ/cm3]
[mJ/cm3]

## Slide 22: Cross - section
A.Priebe, M.Sapinski
10 June 2008
22