MINUTES MEETING CPS-BL CONSOLIDATION. 05/02/2008

AB/BI: B. Dehning, E. Effinger, V. Prieto.

AB/ABO: S. Aumon S. Gilardoni, E. Metral,  Y. Papaphilippou,

AB/OP: B. Mikulec, R. Steerenberg.

- Presentation CPS-BL system and results of the first test with the LHC-BLMs in the PS (V. Prieto AB/BI).

  - The signal of the actual system has been compared with the LHC-BLM system

    - Saturation effect have been observed for fast signals using the ACEM detector (measured with a scope)

    - The ionisation chamber showed no saturation (measured with a scope)

    - The LHC BLM electronics showed a saturation for the sort losses duration (255 bit of CFC counter)

  - Concluding remarks of this measurements:

    - The ACEM detector is not able and cannot be modified to cope with large losses.

    - The ionisation chamber has a linear range which is about 100 times larger as the ACEM, therefore it is better suited to avoid this limitation

    - It is necessary to modify the LHC electronics and software to be able to treat this larger instant losses as allowed at the LHC

  - A test installation with up to 16 channels for the PS will be installed to check further details for a new beam loss system design using spare cables and the LHC electronics (modified upper limit).

- Presentation of the LHC BL specifications report. (B. Dehning, AB/BI). The goal of the talk was to provide an overview of this document (chapters, contents) in order to facilitate the task for the elaboration of the CPS-BL specifications. B. D.  proposed to fill a specification table  (as examples  the specs. of the LHC and LINAC 4 are included). Important items of the table are specification for the timing, thresholds, time resolution, synchronisation, dynamic range, energy dependence…

The transparencies for both presentations are available:

http://cern.ch/blm/CPS_BEAM_LOSS

Overview of the LHC and Linac4 specification

|  | LHC | SPS | PS | PSB | LINAC 4 |
| --- | --- | --- | --- | --- | --- |
| Time resolution [us] | 40 us |  |  |  | 2 |
| Largest loss [Gy/s] | 23 |  |  |  | ? |
| Integration widows | 12 |  |  |  | 1 |
| Max window [s] | 80 |  |  |  | ? |
| Post mortem | yes |  |  |  | yes |
| Post mortem buffer length | 42000 |  |  |  | 42000 |
| Logging frequency [Hz] | 1 |  |  |  | 2 |
| Synchronisation | no |  |  |  | yes |
| Beam permit (thresholds) | yes |  |  |  | yes |
| Beam permit response [ms] | 0.04 |  |  |  | 2 |
| Thresholds energy dependent | yes |  |  |  | no |

- Questions and suggestions raised during the discussion:

- Will it be possibility to measure the residual radiation like in the SPS using the test LHC system. B.D. Yes

- Will it be possible to have access to the data of the test system from the CCC. B.D. yes with the FESA expert application

- Is it possibility to install some mobile BL all around the PS (it depends on the cable availability or/and additional budget.

- Change of the loss monitor locations in order to optimize. V.P. likely for the test in 2008 very difficult, but in general a matter of the availability of space.

- Planning:

In March, a new student starts to look to the needed front end modifications of electronics.

In parallel, the specification table should be filled with the main desired specifications.