Section: AB-BDI-BLM

Redaction: J. Emery

Date: 2 March 2006

# TEST OF THE DAB REV2 V2 DAISY CHAIN

See also Tech. Spec VME Create (EDMS 365170)

The principle of the daisy chain in the DAB is shown in the figure below.

The pull-up at the beginning of the line gives a ‘1’ to the first ‘CL’ (active low). Then the ‘CK’ input must be feed with a frequency to retrigger the internal timer and maintain the ‘1’ to the output ‘Q’. If one of the card is removed or the  FPGA stop sending the frequency to the ‘CK’ input, the line goes to ‘0’ and arrive to the combiner card.

Schematic of the function on the new DAB rev2 v2:

Schematic of the FPGA description for the Daisy chain test

In this design, the signals (timer[x]) enable and disable constantly (2Hz and 4Hz) the frequency generators used to hold the lines (BLM_DCountx) high thought the multvibrator. The result on the P0 connector (and the measurements described below) is a constant variation of these 2 signals (high-low-high..) of 2Hz (nonmaskable) and 4 Hz (masskable). See also test 2.

Schematic of the FPGA description for the Beam Energy lines

Connector P0 with the interesting lines highlighted

from Tech. Spec VME Create (EDMS 365170)

TEST SETUP:

TEST 1:

This is a basic test of removing a card which participates to the daisy chain. First apply a 3.3V on the beginning of the chain (Card ‘1’) (Now the create are modified to have that voltages on the slot 4). Then the DAB (Card ‘3’) should be programmed with the appropriate software.

- Visualise with an oscilloscope the voltage on the card ‘4’ the BLM_DCin 1 and 2, the voltage should be around 3.3V (and pass to 0V then 3.3V with an frequency of 2Hz or 4Hz).

- Without turn off the vme, remouve the card ‘2’, this will cut the 2 lines. The voltage should be 0V

- Connect again the card ‘2’, the voltage should be again as point 1).

TEST 2:

This test control the time constant of the multivibrator retriggerable on the DAB card (U11). For that, the FPGA on the DAB is generating the right frequency (higher than 1MHz better 5MHz) for 0.5s and then stop for 0.5s, the cycle will continue indefinitely. The moment that the FPGA stops retrigger the multivibrator with the frequency to the falling of the signal BLM_DCout_x is the interesting timing to measure.

- Load the FPGA with the appropriate software.

- Connect the oscilloscope as shown on the figure (TEST SETUP page). Channel 1 to the MUX_A out of the DAB card and the channel 2 on the card ‘4’ signal “BLM_DCin_1”.

- Trig to the falling edge of the channel 2, 5us par division.

The result must be around 1s. this timing is quicker that on the Rev1 (was 10us), to speed up the reactivity of the system.

TEST 3:

This test controls the routing and the max frequency usable for the Beam energy lines (called Bus Line 0 to 7 in the document EDMS 365170. For that, these 8 lines are connected to the led on the front panel of the DAB and the first one (Beam Line 0) is connected to the output MUX-A also on the DAB F-P.

- Load the FPGA with the appropriate software.

- Apply 0V and then 3.3V on each of the 8 beam energy lines on the board Test VMEX, you should see the effect on the corresponding led of the DAB card.

- Connect the frequency generator and the oscilloscope as shown. Channel 2 to the MUX_A out of the DAB card and the channel 1 on the Test card signal “Beam energy line 0” (upper pin).

- Trig to the rising edge of the channel 1, 20ns par division.

Then you can try to find the maximal frequency that passes the channel. The result is around 80ns minimal period. In that range, the lines can not be used because of the bad signal integrity behaviour, but the final use will be much slower.

# Text boxes

CH1

CH2

Oscilloscope

Take the correct card with this modification:

8pins connected to the Beam Energy lines 0 (up) to 8 (down)

The 8 LED are connected to the P0 Beam energy lines or called Bus line 0 to 8.

MUX-A output connector (LEMO)

(20ns

MUX-A output

TEST_VMEX

TEST_VMEX

Signal generator

DAB REV2

FREQUENCY GENERATOR

TEST_VMEX

DAB REV1

TEST_VMEX

JUMPERS

BLM_DCout_2

BLM_DCout_1

BLM_DCin_2

BLM_DCin_1

1

2

3

4

VCC = 3.3V

VOLTMETER

+

-

On R6 close to Front panel

Oscilloscope

CH2

CH1

1.2s

Retrigger of the multivibrator on DAB-MUX_A

Daisy chain line BLM_DCin_X of the card 4