Version: not checked with Aurelien

LSS5 MD W42 protons

17 October 2007

Beam type:	LHC25NS 1 (up to 4 batches) protons 450 GeV

Logged data: 	Running Sums -> in ELSA (METER)

BD data -> on bdidev1: /user/bdisoft/development/data/MD42

SPSBCT -> dfs.cern.ch/dfs/Divisions/SL/DIV_SL/BI/PM/DANIEL/MDLSS5_W42/SPSBCT

(TT2 FBCT in the same directory)

11:14		TC1 CH#1 & CH#2 connected to scope in parallel to CFC

11:16		beam for us starts…

Still injection problems (wrong bucket) => large losses during ramp

11:21		Scope timestamp synchronized with CFC timing

NO BEAM, MAINS OFF

11:55		Scope disconnected from TC1 (except HV!) => noise still visible

11:56		Scope disconnected from TC1 => noise considerably smaller

11:58		Scope connected again

12:08		Polling from all cards stopped => much less interruptions of concentrator data

12:08:30	Polling for running sums off => even little better?

12:13:54	FBCT TT2 logging off

12:38		BEAM BACK

12:39		JAW1 to 20mm (was on 30mm = full out)

12:42		BCT saved again

19mm

18mm

12:45:32	TC1 card#1 disconnected

12:46:43	TC3 card#5 disconnected

TC3 card#6 disconnected

12:47?		Cards #5 & 1 SWAPPED

TC3 card#5 CH#2 & 3 connected to scope in parallel

12:56		JAW1 to 10mm

12:59		SWAP to previous configuration!

12:59 		JAW2 to -15mm (was @ -30)

13:00		JAW1 to 9mm

13:03		finally the data saving works..?

13:05		JAW1 to 0mm during FB

JAW2 stays @ -10mm

13:05:20	last injection -> full ½ beam to collimator