Assembly Drawings

LHCBLM__0001: MULTIPLE ELECTRODE BLM ASSEMBLY (the pumping/filling tube has to  be replaced with a cupper tube for pinch off)

LHCBLM__0009: SEM ASSEMBLY (the pumping/filling tube has to be replaced with a cupper tube for pinch off)

LHCBLM__0036: ELECTRICAL CONNECTORS ASSEMBLY

Complete list of drawings

# Table 6 – Complete list of drawings

| QTY | EDMS Number | Title |
| --- | --- | --- |
| 1 | LHCBLM__0001 | MULTIPLE ELECTRODE BLM ASSEMBLY |
| 4 | LHCBLM__0016 type A, variant 1 | MULTIPLE ELECTRODE BLM - TIGHTENERS M4 |
| 2 | LHCBLM__0016 type B, variant 1 | MULTIPLE ELECTRODE BLM - TIGHTENERS M4 |
| 2 | LHCBLM__0013 | ELECTRICAL CONNECTION |
| 1 | LHCBLM__0006 type A | WELDED BLM - BOTTOM COVER |
| 6 | LHCBLM__0007 type C | MULTIPLE ELECTRODE BLM - ELECTRODE SPACERS |
| 183 | LHCBLM__0007 type A | MULTIPLE ELECTRODE BLM - ELECTRODE SPACERS |
| 61 | LHCBLM__0004 | MULTIPLE ELECTRODE BLM - ELECTRODE |
| 2 | LHCBLM__0005 | ALUMINE INSULATOR |
| 1 | LHCBLM__0002 type A | MULTIPLE ELECTRODE BLM - COVER ASSEMBLY (the pumping/filling tube has to be replaced with a cupper tube for pinch off) |
| 3 | LHCBLM__0035 | WELDED SPACER |
| 2 | LHCBLM__0010 | PROTECTION TUBE - FOR COVER |
| 2 | LHCBLM__0008, type A | COVER SPACER |
| 1 | LHCBLM__0003 | MULTIPLE ELECTRODE BLM - COVER |
| 1 | LHCBLM__0009 | SEM ASSEMBLY |
| 6 | LHCBLM__0007 type A | MULTIPLE ELECTRODE BLM - ELECTRODE SPACERS |
| 2 | LHCBLM__0016 type A, variant 2 | MULTIPLE ELECTRODE BLM - TIGHTENERS M4 |
| 2 | LHCBLM__0016 type A, variant 3 | MULTIPLE ELECTRODE BLM - TIGHTENERS M4 |
| 1 | LHCBLM__0016 type B, variant 2 | MULTIPLE ELECTRODE BLM - TIGHTENERS M4 |
| 1 | LHCBLM__0016 type B, variant 3 | MULTIPLE ELECTRODE BLM - TIGHTENERS M4 |
| 2 | LHCBLM__0013 | ELECTRICAL CONNECTION |
| 1 | LHCBLM__0006 type B | WELDED BLM - BOTTOM COVER |
| 6 | LHCBLM__0007 type B | MULTIPLE ELECTRODE BLM - ELECTRODE SPACERS |
| 3 | LHCBLM__0004 | MULTIPLE ELECTRODE BLM - ELECTRODE |
| 1 | LHCBLM__0005 | ALUMINE INSULATOR |
| 1 | LHCBLM__0002 type B | MULTIPLE ELECTRODE BLM - COVER ASSEMBLY (the pumping/filling tube has to be replaced with a cupper tube for pinch off) |
| 3 | LHCBLM__0035 | WELDED SPACER |
| 2 | LHCBLM__0010 | PROTECTION TUBE - FOR COVER |
| 2 | LHCBLM__0008, type B | COVER SPACER |
| 1 | LHCBLM__0003 | MULTIPLE ELECTRODE BLM - COVER |
| 1 | LHCBLM__0036 | ELECTRICAL CONNECTORS ASSEMBLY |
| 1 | LHCBLM__0037 | ELECTRICAL CONNECTION EXTERNAL PLATE |
| 1 | LHCBLM__0038 | ELECTRICAL CONNECTION - EXTERNAL TUBE |
| 1 | LHCBLM__0039 | ELECTRICAL CONNECTION - FEEDTHROUGH PROTECTION |

List of Material provided by CERN

For the Multiple electrode BLM Detector

# Table 7 – 	List of Material provided by CERN for the ionization chamber with parallel plates

| MULTIPLE ELECTRODE BLM |
| --- |
| Materiel |
| QTY | SCEM |  | Remarques |  |
| 1 | 39.38.05.088.2 | Multiple electrode (0001) | round tube 304 | ext 88.9mm,Ep 2mm, L 500mm |
| 2 | 47.62.82.145.0 |  | vis st 6 pc chan inox M3 *4 |  |
| 2 | 44.59.32.050.0 |  | vis cyl inox A4 316 M3 *6 |  |
| 2 | 19.63.30.128.9 |  | alumina tube |  |
| 1 | N.S |  | Compressing spring 1.4310 ferroflex |  |
| 6 | N.S |  | spring washer f 8 4.2-0.3 |  |
| 6 | 47.43.77.040.1 |  | hex nuts inox Al 316 0.8 M4 |  |
| 4 | 44.57.10.404.4 | Tighteners (0016) | inox ronds 304 M4 | L = 404mm, f =8mm |
| 4 | N.S |  | washer (welded) |  |
| 2 | 44.57.10.404.4 |  | inox ronds 304 M4 | L = 404mm, f =8mm |
| 2 | 44.57.10.408.0 | Electrical connection (0013) | inox ronds 304 M4 | L = 20mm, f = 8 mm |
| 1 | 39.36.05.430.6 | Bottom cover (0006) | tube inox 316 d12 *10 | L =24mm, f = 10 |
| 1 | 44.59.32.040.2 |  | sheet stain. Steel 304 L | f = 89 mm, Thick 4mm |
| 6 | 39.36.05.380.9 | Electrode spacer (0007) | tube inox 316 *5 | L =5.75mm f = 6mm |
| 183 | 39.36.05.380.9 |  | tube inox 316 *5 | L =12mm f = 6mm, ( |
| 61 | 44.02.30.005.0 | Electrode (0004) | tole ALSI 1 MG | f = 75 mm thick =0.5mm, 1.3dm2 |
| 2 | N.S | Alumina insulator (0005) | AL2O3 |  |
| 1 | N.S | Cover assembly (0002) | Pinch-off |  |
| 2 | N.S |  | Feedthrough ceramseal |  |
| 3 | 44.57.10.408.0 | Welded spacer (0035) | inox ronds 304L | L = 10 mm, f = 8mm |
| 2 | 39.36.05.490.4 | Protection tube for cover (0010) | inox ronds 304L | L = 23 mm, f = 18mm |
| 2 | 44.57.10.418.8 | Cover spacer (0008) | inox ronds 304L | L = 46 mm, f = 18mm |
| 1 | 44.59.40.060.1 | Cover (0003) | tole inox 316l | f = 86mm, thick 6 mm |
| 2 | 47.62.96.101.1 | Electrical connectors assembly(0036) | inox head hex point scr M3*5 |  |
| 3 | 47.78.09.004.1 |  | rondelle contact M4 |  |
| 6 | 47.43.77.040.1 |  | hex nuts inox A4 316 M4 |  |
| 1 | 39.64.05.036.3 |  | Rond tube AlMgSi hard | 12*15 |
| 3 | 47.38.77.040.8 |  | thread rods A4 316 M4 | L = 90 mm |
| 3 | 39.64.05.012.1 |  | tube AlMgSi hard 4*7 | L = 61 mm |
| 2 | 09.41.25.160.9 |  | BNC HT Polypenco SHV 5KV |  |
| 1 | 09.46.11.360.4 |  | BNC 50ohm, teflon |  |
| 3 | 09.46.11.520.6 |  | Cosse à souder BNC 50 ohm |  |
| 1 | 04.01.61.680.4 |  | Fils cablage souple | L= 100mm, 0,5mm2 |
| 1 | N.S |  | Resistance | 10M1W |
| 1 | N.S |  | Condensateur | 0.47uF, 2000V |
| 1 | 39.36.05.505.4 | Electrical connection feethrough( 0039) | tube inox 316 | f = 20 mm, L 45mm |
| 1 | 39.39.05.088.2 | Electrical connection Ext. tube( 0038) | rond tube 304 L | F = 88.9 mm, L 83mm, thick 2mm |
| 1 | 44.02.07.090.4 | Electrical connection Ext. plate( 0037) | rond AlSiMgMn T.REV.Hard | F = 84mm, thick= 6mm |

For the SEM Detector

# Table 8 – 	List of Material provided by CERN for the SEM

| SEM |
| --- |
| Materiel |
| QTY | SCEM |  | Remarques |  |
| 1 | 39.38.05.088.2 | SEM (0009) | round tube 304 | ext 88.9mm,Ep 2mm, L 120mm |
| 2 | 47.62.82.145.0 |  | vis st 6 pc chan inox M3 *4 |  |
| 2 | 44.59.32.050.0 |  | vis cyl inox A4 316 M3 *6 |  |
| 2 | 19.63.30.128.9 |  | alumina tube |  |
| 22 | 47.43.77.040.1 |  | hex nuts inox Al 316 0.8 M4 |  |
| 4 | 44.57.10.404.4 | Tighteners (0016) | inox ronds 304 M4 | L = 40mm, f =8mm |
| 6 | N.S |  | washer (welded) |  |
| 2 | 44.57.10.404.4 |  | inox ronds 304 M4 | L = 40mm, f =8mm |
| 2 | 44.57.10.408.0 | Electrical connection (0013) | inox ronds 304 M4 | L = 20mm, f = 8 mm |
| 1 | 39.36.05.430.6 | Bottom cover (0006) | tube inox 316 d12 *10 | L =24mm, f = 10 |
| 1 | 44.59.32.040.2 |  | sheet stain. Steel 304 L | f = 89 mm, Thick 4mm |
| 6 | 39.36.05.380.9 | Electrode spacer (0007) | tube inox 316 *5 | L = 18.25mm f = 6mm |
| 3 | 44.02.30.005.0 | Electrode (0004) | tole ALSI 1 MG | f = 75 mm thick =0.5mm, 1.3dm2 |
| 1 | N.S | Alumina insulator (0005) | AL2O3 |  |
| 1 | N.S | Cover assembly (0002) | Pinch-off |  |
| 2 | N.S |  | Feedthrough ceramseal |  |
| 3 | 44.57.10.408.0 | Welded spacer (0035) | inox ronds 304L | L = 10 mm, f = 8mm |
| 2 | 39.36.05.490.4 | Protection tube for cover (0010) | inox ronds 304L | L = 23 mm, f = 18mm |
| 2 | 44.57.10.418.8 | Cover spacer (0008) | inox ronds 304L | L = 46 mm, f = 18mm |
| 1 | 44.59.40.060.1 | Cover (0003) | tole inox 316l | f = 86mm, thick 6 mm |
| 2 | 47.62.96.101.1 | Electrical connectors assembly(0036) | inox head hex point scr M3*5 |  |
| 3 | 47.78.09.004.1 |  | rondelle contact M4 |  |
| 6 | 47.43.77.040.1 |  | hex nuts inox A4 316 M4 |  |
| 1 | 39.64.05.036.3 |  | Rond tube AlMgSi hard | 12*15 |
| 3 | 47.38.77.040.8 |  | thread rods A4 316 M4 | L = 90 mm |
| 3 | 39.64.05.012.1 |  | tube AlMgSi hard 4*7 | L = 61 mm |
| 2 | 09.41.25.160.9 |  | BNC HT Polypenco SHV 5KV |  |
| 1 | 09.46.11.360.4 |  | BNC 50ohm, teflon |  |
| 3 | 09.46.11.520.6 |  | Cosse à souder BNC 50 ohm |  |
| 1 | 04.01.61.680.4 |  | Fils cablage souple | L= 100mm, 0,5mm2 |
| 1 | N.S |  | Resistance | 10M1W |
| 1 | N.S |  | Condensateur | 0.47uF, 2000V |
| 1 | 39.36.05.505.4 | Electrical connection feethrough( 0039) | tube inox 316 | f = 20 mm, L 45mm |
| 1 | 39.39.05.088.2 | Electrical connection Ext. tube( 0038) | rond tube 304 L | F = 88.9 mm, L 83mm, thick 2mm |
| 1 | 44.02.07.090.4 | Electrical connection Ext. plate( 0037) | rond AlSiMgMn T.REV.Hard | F = 84mm, thick= 6mm |

For the electronics box with filter

# Table 10 – 	List of Material provided by CERN for the electronics box

XXXXXXXXX