Minutes of meeting 19.04.2006 at 9:30 h.

Quench levels of the magnets in the LSS5 
(i.e. D2, Q4 and Q6 and the associated dipole correctors).

Present:  Dariusz Bocian, Daniela Macina, Richard Hall-Wilton, Vadim Talanov.

# D. Macina: Short introduction to the task.

D. Macina has presented the objectivities of work. The operation of the TOTEM Roman Pots in the LHC line could cause the showers of high intensity secondaries. The main task of this work is to check the intensity of the secondaries and its influence on the superconducting magnets and the corresponding signals in the BLMs. The point is whether these particles might deposit sufficient energy in the magnet coil to quench magnets downstream of the roman pots.

The purpose of this meeting is to determine how to evaluate what the results of the simulations for energy deposits in the magnets mean as a fraction of the magnet quench limits.  This implies additionally checking that the simulation results are available in a form that can be used to convert these into fractions of the quench limit i.e. the grid chosen is appropriate for evaluating this limit.

# D. Bocian: Overview of enthalpy limit of all magnets for injection 
and collision energy and heat transfer in the magnets.

## A schematic view of the heat transport in the magnet.

## Heat transfer in the coil

Fig. 1 Heat transport in the superconducting cables and insulation

## Entalpy limit

| Entalpy limit [mJoule/cm3] |
| --- |
|  |  | Beam energy = 450 GeV | Beam energy = 7000 GeV |
|  |  | Fast perturbation | Slow perturbation | Fast perturbation | Slow perturbation |
| Magnet | Temp | <100 μs | >100 ms | <100 μs | >100 ms |
| MB Type-1 | 1.9K | 31,29 | 148,53 | 0,93 | 56,26 |
| MB Type-2 | 1.9K | 29,24 | 141,21 | 0,90 | 53,70 |
| MQ Type-3 | 1.9K | 29,45 | 150,69 | 1,41 | 72,09 |
| MQM Type-7 | 1.9K | 30,31 | 127,78 | 1,06 | 50,11 |
| MQM Type-7 | 4.5K | 28,22 | 47,58 | 1,63 | 6,35 |
| MQY Type-5 | 4.5K | 28,43 | 48,55 | 2,46 | 8,78 |
| MQY Type-6 | 4.5K | 32,06 | 57,76 | 4,95 | 15,84 |
| MCB corr-1 | 1.9K | 23,21 | 23,21 | 4,77 | 4,77 |
| MCBC corr-2 | 1.9K | 23,13 | 23,13 | 4,20 | 4,20 |
| MCBC corr-2 | 4.5K | 21,60 | 21,60 | 5,69 | 5,69 |
| MCBY corr-2 | 1.9K | 23,30 | 23,30 | 5,21 | 5,21 |
| MCBY corr-2 | 4.5K | 21,51 | 21,51 | 5,28 | 5,28 |
| MCBXH corr-4 | 1.9K | 33,11 | 33,11 | 10,91 | 10,91 |
| MCBXV corr-4 | 1.9K | 33,22 | 33,22 | 11,66 | 11,66 |
| MCD corr-3 | 1.9K | 32,88 | 32,88 | 10,65 | 10,65 |
| MCO corr-2 | 1.9K | 23,72 | 23,72 | 7,64 | 7,64 |
| MCOSX corr-2 | 1.9K | 23,98 | 23,98 | 9,46 | 9,46 |
| MCOX corr2 | 1.9K | 23,98 | 23,98 | 9,37 | 9,37 |
| MCS corr-3 | 1.9K | 32,99 | 32,99 | 12,27 | 12,27 |
| MCSSX corr-2 | 1.9K | 23,98 | 23,98 | 9,50 | 9,50 |
| MCSX corr-2 | 1.9K | 23,81 | 23,81 | 7,02 | 7,02 |
| MCTX corr-2 | 1.9K | 23,30 | 23,30 | 4,89 | 4,89 |
| MO corr-3 | 1.9K | 32,76 | 32,76 | 10,55 | 10,55 |
| MQS corr-3 | 1.9K | 32,20 | 32,20 | 5,81 | 5,81 |
| MQSX corr3 | 1.9K | 32,20 | 32,20 | 6,32 | 6,32 |
| MQT corr-3 | 1.9K | 32,20 | 32,20 | 5,81 | 5,81 |
| MQTLI corr-3 | 1.9K | 32,20 | 32,20 | 5,81 | 5,81 |
| MS corr-3 | 1.9K | 32,08 | 32,08 | 5,00 | 5,00 |
| MSS corr-3 | 1.9K | 32,08 | 32,08 | 5,00 | 5,00 |
| MQTLH corr-3 | 4.5K | 29,72 | 29,72 | 5,69 | 5,69 |

The names Type-1 to Type-6 and corr-1 to corr-4 corresponds to the cable types in the coils of the magnets (Table 3 and Table 4). When two types of the cables appear with the same name of the magnet, it means that coil consists of two types of the cables. In case of LHC magnets, there are two types of cables used in:

- two-layers coil of MB (main dipole) magnet: cable Type-1 is inner layer and cable Type-2 is outer layer,

- four layers MQY magnet, first (inner) layer is made from cable Type-6, second – central part is made from cable Type-5 and sides from cable Type-6 and layers 3 and 4 of coil is made from cable Type-5. This is demonstrated in figure 2.

Fig. 2 Types and locations of superconducting cables in MQY magnet.

These quench limits are given for the peak magnetic field strength in the magnets. This then gives a worst case scenario – as the magnetic field varies considerably within the coil. There is also the issue that the field in the magnet whilst running will be below the peak strength – however for the nominal optics it is expected to be a significant fraction of the full strength.

In the table, it can be seen that for some magnets – MB, MQ, MQM, MQY – there are differences between the fast and slow perturbations in the quench limits. This is because the magnets are «wet», i.e. liquid helium are inside the cables and flows through the coils. For the other magnets, including all the correctors, they are «dry», and there is no helium flow through the coils. The helium flow through the coils allows significant cooling of the cables – hence the large differences between the 2 sets of numbers. For time periods between the 2 extremes, there will be a partial affect – this is non-trivial to calculate as it depends upon modelling the superfluid He and its properties.

## Superconducting cable characteristics

Table 1 Cable characteristic

| Cable type | Strand type | #strands | A-cable (mm2) | Cu (mm2) | NbTi (mm2) | He (mm2) | Insulation (mm2) | Ic at 6T (A) | Ic at 7T (A) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Type-1 | 1 | 28 | 25.489 | 15.871 | 9.618 | 2.005 | 5.460 | 20080 | 15300 |
| Type-2 | 2 | 36 | 19.974 | 13.203 | 6.771 | 1.494 | 5.327 | 15139 | 11139 |
| Type-3 | 2 | 36 | 19.974 | 13.203 | 6.771 | 1.627 | 4.510 | 15139 | 11139 |
| Type-4 | 5 | 36 | 6.646 | 4.229 | 2.417 | 0.429 | 1.885 | 5505 | 3962 |
| Type-5 | 5 | 34 | 6.290 | 4.003 | 2.287 | 0.422 | 1.790 | 5285 | 3864 |
| Type-6 | 6 | 22 | 9.432 | 5.240 | 4.192 | 0.834 | 1.872 | 9452 | 7041 |
| Type-7 | 5 | 36 | 6.646 | 4.229 | 2.417 | 0.429 | 1.885 | 5505 | 3962 |

Table 2 Characteristic of the corrector cables

| Cable type | A-cable (mm2) | Cu (mm2) | NbTi (mm2) | Insulation (mm2) | Ic at 6T (A) | Ic at 7T (A) |
| --- | --- | --- | --- | --- | --- | --- |
| Corr-1 | 0.110 | 0.088 | 0.022 | 0.0382 | 48.6 | 36.5 |
| Corr-2 | 0.214 | 0.172 | 0.043 | 0.0630 | 77.2 | 56.7 |
| Corr-3 | 0.689 | 0.424 | 0.265 | 0.2232 | 557.4 | 409.6 |
| Corr-4 | 1.301 | 0.800 | 0.500 | 0.3000 | >930 | 691.8 |

Table 3 Magnet characteristic and cable types used in the production.

| Magnet type | Cable type | Op-T (K) | I (A) | Pick-field (T) |
| --- | --- | --- | --- | --- |
| MB | Type-1 | 1.9 | 11850 | 8.58 |
| MB | Type-2 | 1.9 | 11850 | 7.41 |
| MQ | Type-3 | 1.9 | 11870 | 6.85 |
| MQM | Type-7 | 1.9 | 5390 | 6.30 |
| MQM | Type-7 | 4.5 | 4310 | 5.04 |
| MQMC | Type-4 | 1.9 | 5390 | 6.30 |
| MQML | Type-4 | 1.9 | 5390 | 6.30 |
| MQML | Type-4 | 4.5 | 4310 | 5.04 |
| MQY | Type-5 | 4.5 | 3610 | 5.13 |
| MQY | Type-6 | 4.5 | 3610 | 6.16 |
| MBRB | Type-R1 | 4.5 | 5520 | 3.85 |
| MBRC | Type-R1 | 4.5 | 6000 | 4.18 |
| MBRS | Type-R1 | 4.5 | 5520 | 3.85 |
| MBX | Type-R1 | 1.9 | 5800 | 4.18 |
| MQXA | Type-K1 | 1.9 | 6450 | 8.23 |
| MQXA | Type-K2 | 1.9 | 6450 | 8.23 |
| MQXB | Type-F1 | 1.9 | 10630 | 7.34 |
| MQXB | Type-F1 | 1.9 | 10630 | 7.34 |

Table 4 Corrector magnet characteristic and cable types used in the production.

| Magnet type | Cable type | Op-T (K) | I (A) | Pick-field (T) |
| --- | --- | --- | --- | --- |
| Orbit correctors |
| MCB(H&V) | Corr-1 | 1.9 | 55 | 3.15 |
| MCBC(H&V) | Corr-2 | 1.9 | 100 | 3.65 |
| MCBC(H&V) | Corr-2 | 4.5 | 74 | 2.68 |
| MCBY(H&V) | Corr-2 | 1.9 | 88 | 3.60 |
| MCBY(H&V) | Corr-2 | 4.5 | 72 | 2.96 |
| MCBXH | Corr-4 | 1.9 | 550 | 4.02 |
| MCBXV | Corr-4 | 1.9 | 550 | 3.71 |
| Multipole correctors |
| MCD | Corr-3 | 1.9 | 550 | 2.40 |
| MCO | Corr-2 | 1.9 | 100 | 2.00 |
| MCOSX | Corr-2 | 1.9 | 100 | 1.34 |
| MCOX | Corr-2 | 1.9 | 100 | 1.37 |
| MCS | Corr-3 | 1.9 | 550 | 1.90 |
| MCSSX | Corr-2 | 1.9 | 100 | 1.32 |
| MCSX | Corr-2 | 1.9 | 50 | 4.20 |
| MCTX | Corr-2 | 1.9 | 80 | 4.10 |
| Lattice correctors |
| MO | Corr-3 | 1.9 | 550 | 2.43 |
| MQS | Corr-3 | 1.9 | 550 | 4.10 |
| MQSX | Corr-3 | 1.9 | 550 | 3.94 |
| MQT | Corr-3 | 1.9 | 550 | 4.10 |
| MQTLI | Corr-3 | 1.9 | 550 | 4.10 |
| MS | Corr-3 | 1.9 | 550 | 4.37 |
| MSS | Corr-3 | 1.9 | 550 | 4.37 |
| Q6 at IP6 |
| MQTLH | Corr-3 | 4.5 | 400 | 4.10 |

Table 5 Characteristic data of the “CERN” superconducting cables.

|  | Units | Cable 1 | Cable 2 | Cable 3 | Cable 4 | Cable 5 | Cable 6 | Cable 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Strand diameter | mm | 1.065 | 0.825 | 0.825 | 0.48 | 0.48 | 0.74 | 0.48 |
| Number of strands |  | 28 | 36 | 36 | 36 | 34 | 22 | 36 |
| Average r = Cu/NbTi |  | 1.65 | 1.95 | 1.95 | 1.75 | 1.75 | 1.25 | 1.75 |
| Keystone angle | deg | 1.25 | 0.9 | 0.9 | 0.91 | 0.9 | 1.72 | 0.91 |
| Cable width (bare) | mm | 15.1 | 15.1 | 15.1 | 8.8 | 8.3 | 8.3 | 8.8 |
| Cable mid-thickness (bare) | mm | 1.9 | 1.48 | 1.48 | 0.84 | 0.845 | 1.275 | 0.84 |
| Cable inner thickness (bare) | mm | 1.7353 | 1.3614 | 1.3614 | 0.7701 | 0.7798 | 1.1504 | 0.7701 |
| Cable outer thickness (bare) | mm | 2.0647 | 1.5986 | 1.5986 | 0.9099 | 0.9102 | 1.3996 | 0.9099 |
| Transposition pitch | mm | 115.00 | 100.00 | 100.00 | 66.00 | 66.00 | 66.00 | 66.00 |
| Radial insulation thickness | mm | 0.15 | 0.15 | 0.13 | 0.08 | 0.08 | 0.08 | 0.08 |
| Azimuthal insulation thickness | mm | 0.12 | 0.13 | 0.11 | 0.08 | 0.08 | 0.08 | 0.08 |
| Cable width (ins.) | mm | 15.4 | 15.4 | 15.36 | 8.96 | 8.46 | 8.46 | 8.96 |
| Cable thickness (ins.) | mm | 2.14 | 1.74 | 1.70 | 1.00 | 1.005 | 1.435 | 1.00 |
| Cable inner thickness (ins.) | mm | 1.9720 | 1.6190 | 1.5794 | 0.9288 | 0.9386 | 1.3080 | 0.9288 |
| Cable outer thickness (ins.) | mm | 2.3080 | 1.8610 | 1.8206 | 1.0712 | 1.0714 | 1.5620 | 1.0712 |
| Jc (B[T], Tref) | A/mm2 | 1433.3 (9.0T,1.9K) | 1953 (9.0T,1.9K) | 1953 (9.0T,1.9K) | 2800 (5T,4.2K) | 2800 (5T,4.2K) | 2670 (5T,4.2K) | 2800 (5T,4.2K) |
| Cable length | m | 460 | 740 | 740 | 740 | 775 | 710 | 540 |

Table 6 Characteristic of the corrector cables. Insulation material - PVA enamel. Superconductor NbTi with Ti=47% by weight.

|  | Units | Corr-1 | Corr-2 | Corr-3 | Corr-4 |
| --- | --- | --- | --- | --- | --- |
| Overall dimensions (ins) | mm | Ø 0.435 | 0.38×0.73 | 0.73×1.25 | 0.97×1.65 |
| Metal dimensions | mm | Ø 0.375 | 0.32×0.67 | 0.61×1.13 | 0.85×1.53 |
| Insulation thickness | mm | 0.03 | 0.03 | 0.06 | 0.06 |
| Cu/NbTi volume ratio |  | 4.1 | 4.1 | 1.68 | 1.65 |
| Nr of filaments |  | 684 | 1110 | 7068 | 8898 |
| Filament diameter | μm | 6.4 | 6.5 | 6.7 | 8.3 |
| Critical current at 4.2K, 5T | Perpendicular to wire axis | A | >55 |  |  |  |
|  | Perpendicular to broad face | A |  | >100 | >630 | >1190 |
|  | Parallel to broad face | A |  | >110 | >700 | >1320 |

Table 7 Characteristic data of the “non-CERN” superconducting cables.

|  |  | MQXA KEK cables | MQXB Fermilab cables | MB(Rx)(X) RHIC cables |
| --- | --- | --- | --- | --- |
|  | Units | K1 | K2 | F1 | F2 | R1 |
| Strand diameter | mm | 0.815 | 0.735 | 0.808 | 0.65 | 0.648 |
| Number of strands |  | 27 | 30 | 37 | 46 | 30 |
| Average r = Cu/NbTi |  | 1.2 | 1.9 | 1.3 | 1.8 | 1.8 |
| Keystone angle | deg | 2.309 | 1.319 | 1.079 | 0.707 | 1.2 |
| Cable width (bare) | mm | 11 | 11 | 15.4 | 15.4 | 9.73 |
| Cable mid-thickness (bare) | mm | 1.487 | 1.34 | 1.456 | 1.146 | 1.166 |
| Cable inner thickness (bare) | mm | 1.2654 | 1.2134 | 1.3110 | 1.0510 | 1.0641 |
| Cable outer thickness (bare) | mm | 1.7086 | 1.4666 | 1.6010 | 1.2410 | 1.2679 |
| Transposition pitch | mm |  |  |  |  |  |
| Radial insulation thickness | mm |  |  |  |  |  |
| Azimuthal insulation thickness | mm |  |  |  |  |  |
| Cable width (ins.) | mm |  |  |  |  |  |
| Cable thickness (ins.) | mm |  |  |  |  |  |
| Cable inner thickness (ins.) | mm |  |  |  |  |  |
| Cable outer thickness (ins.) | mm |  |  |  |  |  |
| Jc (B[T], Tref) | A/mm2 | 2200 (6T, 4.2K) | 2160 (6T, 4.2K) | 2750 (5T, 4.2K) | 2750 (5T, 4.2K) | 2500 (5T, 4.2K) |
| Cable length | m |  |  |  |  |  |

Table 8 Free volume calculation – bare. Volume is normalized to mm2. Volume0
is an additional volume calculation for non-deformed cable using strand cross section only.

|  | Units | Type-1 | Type-2 | Type-3 | Type-4 | Type-5 | Type-6 | Type-7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Volume0 (strand) (bare) | mm2 | 25.789 | 20.103 | 20.103 | 6.742 | 6.344 | 9.757 | 6.742 |
| Volume1 (m,ρ) (bare) | mm2 | 25.489 | 19.974 | 19.974 | 6.646 | 6.290 | 9.432 | 6.646 |
| Volume2(α,h,l)(bare) | mm2 | 28.688 | 22.347 | 22.347 | 7.392 | 7.013 | 10.581 | 7.392 |
| Free Volume (bare) | mm2 | 3.199 | 2.373 | 2.373 | 0.746 | 0.723 | 1.149 | 0.746 |
| Free Volume (bare) | % | 11.152 | 10.621 | 10.621 | 10.090 | 10.313 | 10.860 | 10.090 |

## Heat transfer in the magnets

## A schematic view of the heat extraction from the quadrupole magnet at the temperature T=1.9 K (left) and T=4.5 K (right) is presented in the Fig. 3.

Fig. 3 A simple sketch of the heat transfer in the quadrupole at T=1.9 K (left) and T=4.5K(right).

### Heat extraction from the SC cables at T=1.9 K

#### inner layer: heat goes from the cables to the helium channel between cold bore and superconducting coil, and further mainly by the channels between the laminations.

#### outer layer: heat goes through insulation between two layers of the cables and then through the inner layer to the helium channel between cold bore and superconducting coil, and further mainly by the channels between the laminations.

# V. Talanov, Richard Hall-Wilton: Issues arising

# The magnets most likely to be affected are those just downstream of the roman pot stations. The station at 148m is most likely to affect D2, Q4, and the correctors, MCYA/B, in the D2-Q4 cryostat. The second station to be installed is most likely to affect Q6, and its correctors, MCBCB. The data is available for all of these magnet types in the table presented earlier. Except for D2.

There is no data for D2 in the table, as there are as yet no samples of cable available from RHIC. It should be possible to fill in the numbers for the fast losses in this table, however it will probably be a long time before there will be data available on the slow losses, as this requires measurements to be done on the He flow within the strands.

# The effect of the optics was discussed, as mentioned before, the quench limit is expected to depend upon the field strength in the coil. At nominal optics the field strength is expected to be close to the peak field strength, however for alternative optics, eg 2m, 19m, TOTEM optics, the fields could be considerably lower. D2 will not be expected, as the field in the dipole will depend only upon the beam energy. However the quadrapoles and the correctors might be affected.

The tables presented in section 2.4 allow a cross check of the validity of the assumption, used in {4}, that the coils can be approximated by copper for the purposes of simulating the energy deposition in them. In the case of the main dipoles it was found that the average atomic weight was very close to that of copper.

# Summary:

- The data provided in these minutes should suffice to evaluate the fraction of quench limit from any given energy deposit in the coils for all magnets except D2.

- It is necessary to calculate enthalpy limit for the non-CERN magnets. Of interest in particular here - D2. (Other magnets, eg Q1, Q2, Q3, of interest for other studies). In terms of the brief of the study here, an approximate number for the quench limit from a fast perturbation would suffice.

- Additional factors like optics, slow/fast perturbation and cable type location have been flagged. Some comment should be made on these effects in the course of the investigations.

# References:

- 1. A Simplified Cryogenic Distribution Scheme for the Large Hadron Collider / Chorowski, M; Erdt, W K; Lebrun, P; Riddone, G; Serio, L; Tavian, L; Wagner, U; Van Weelderen, R, LHC Project Report 143, 1997,

- Cooling Strings of Superconducting Devices below 2 K : the Helium II Bayonet Heat Exchanger / Lebrun, P; Serio, L; Tavian, L; Van Weelderen, R, LHC Project Report 144, 1997,

- Heat transfer in electrical insulation of LHC cables cooled with superfluid helium /  Meuris, C.; Baudouy, B.; Leroy, D.; Szeless, B., Cryogenics, v. 39, iss. 11, p. 921-931.

- BFPP Losses and Quench Limit for LHC Magnets / R.Bruce, S.Gilardoni, J.M.Jowett, LHC Project Report 379, 2005.

- Quench levels and transient beam losses in LHC magnets/ Jeanneret J.B. et al., LHC Project Report 44, CERN, 1996.

# Text boxes

Cryogenic System

Helium

Insulation

Cu

Helium

NbTi

Insulation

Spacers

Conductors

Second layer

First layer

Vacuum tube

3