| AB-CO-MI 08-05 0v5 (Engineering) AB-CO-MI 883620 2008-02-01 |
| --- |
| ENGINEERING SPECIFICATION |
| THRESHOLDS FOR THE SAFE MACHINE PARAMETERS SYSTEMS OF SPS AND LHC |
| Abstract This document specifies the thresholds to be used in the generation of mission critical flags in the Safe Machine Parameters System of both the SPS and LHC. |
| Prepared by : B. Todd AB/CO B. Puccio AB/CO R. Schmidt AB/CO I. Romera AB/CO | Checked by : J. Wenninger V. Kain | Approval Leader: R. Schmidt |
| History of Changes |
| Rev. No. | Date | Pages | Description of Changes |
| 0.0 0.1 0.2 0.3 0.4 0.5 | 2007-11-15 2007-11-22 2007-11-23 2007-11-24 2007-11-24 2008-02-01 | All All SPS Thresholds All SBF Table Forcing | First draft. Released for first comments. Changed the values of the E400 and E450 thresholds [JW]. Reformatted file, added full table for LHC SBF [IRR]. Corrected typo Removed obsolete references to forcing registers. |

Table of Contents (not compulsory, can be removed)

1.	SPS UNIQUE THRESHOLDS	4

2.	LHC UNIQUE THRESHOLDS	5

2.1	FULL LISTING OF SAFE_BEAM_FLAG THRESHOLDS	6

3.	FORCING and TUNING	8

3.1	TUNING THE SPS PROBE BEAM FLAG	8

3.2	FORCING LHC Safe Beam Flag FALSE	8

# SPS UNIQUE THRESHOLDS

Note that Energy values must be a multiple of 120MeV.

| Threshold Name | Typical value [units] | Function [Accelerator] |
| --- | --- | --- |
| E400_UPPER_LIMIT | 402.600 [GeV] | This is the upper limit for the Energy 400 flag to be considered TRUE [SPS] |
| E400_LOWER_LIMIT | 397.440 [GeV] | This is the lower limit for the Energy 400 flag to be considered TRUE [SPS] |
| Formula for E400_FLAG (only in the SPS): E400_FLAG = TRUE when (ENERGY ≥ E400_LOWER_LIMIT) AND (ENERGY ≤ E400_UPPER_LIMIT) else FALSE |
| E450_UPPER_LIMIT | 455.040 [GeV] | This is the upper limit for the Energy 450 flag to be considered TRUE [SPS] |
| E450_LOWER_LIMIT | 444.960 [GeV] | This is the lower limit for the Energy 450 flag to be considered TRUE [SPS] |
| Formula for E450_FLAG (only in the SPS): E450_FLAG = TRUE when (ENERGY ≥ E450_LOWER_LIMIT) AND (ENERGY ≤ E450_UPPER_LIMIT) else FALSE |
| PROBE_BEAM_LIMIT | 1E11 [p] | This is the limit below which the Probe Beam Flag will be TRUE [SPS] |
| Formula for PROBE_BEAM_FLAG (only in the SPS): PROBE_BEAM_FLAG = TRUE when (INTENSITY ≤ PROBE_BEAM_LIMIT) else FALSE N.B. it is proposed to ‘tune’ this flag, see the last page. |
| SAFE_BEAM_FLAG_LIMIT | 1E12 [p] | This is the limit below which the Safe Beam Flag will be TRUE [SPS] |
| Formula for SAFE_BEAM_FLAG (only in the SPS): SAFE_BEAM_FLAG = TRUE when (INTENSITY ≤ SAFE_BEAM_FLAG_LIMIT) else FALSE |

# LHC UNIQUE THRESHOLDS

Note that Energy values must be a multiple of 120MeV.

| Threshold Name | Typical value [units] | Function [Accelerator] |
| --- | --- | --- |
| SAFE_BEAM_FLAG_1 to SAFE_BEAM_FLAG_64 | 1 = 1E12 … 64 = 1E10 | This is the range of limits below which the Safe Beam Flag will be TRUE [LHC] |
| Formula for SAFE_BEAM_FLAG (only in the LHC): Select BIN according to ENERGY. SAFE_BEAM_FLAG = TRUE when (INTENSITY ≤ SAFE_BEAM_FLAG_N) else FALSE N.B. There is a unique SAFE_BEAM_FLAG for each beam. |
| BEAM_PRESENCE_LIMIT | 5E9 [p] | This is the limit above which the Beam Presence Flag will be TRUE [LHC] |
| Formula for BEAM_PRESENCE_FLAG (only in the LHC): BEAM_PRESENCE_FLAG = TRUE when (INTENSITY ≥ BEAM_PRESENCE_LIMIT) else FALSE N.B. There is a unique BEAM_PRESENCE_FLAG for each beam. |
| ENERGY_7TEV_UPPER_LIMIT | 7001.040 [GeV] | This is the limit above which the Stable Beam Flag and the Moveable Devices In Flag will be forced FALSE [LHC] |
| ENERGY_7TEV_LOWER_LIMIT | 6999.000 [GeV] | This is the limit below which the Stable Beam Flag and the Moveable Devices In Flag will be forced FALSE [LHC] |
| Formula for MOVEABLE_DEVICES_IN_FLAG (only in the LHC): MOVEABLE_DEVICES_IN_FLAG = TRUE when ((ENERGY ≤ ENERGY_7TEV_UPPER_LIMIT) AND (ENERGY ≥ ENERGY_7TEV_LOWER_LIMIT) ) AND ((MODE = “STABLE_BEAMS”) OR (MODE = “UNSTABLE BEAMS”)) Formula for STABLE_BEAMS_FLAG (only in the LHC): STABLE_BEAMS_FLAG = TRUE when ((ENERGY ≤ ENERGY_7TEV_UPPER_LIMIT) AND (ENERGY ≥ ENERGY_7TEV_LOWER_LIMIT) ) AND (MODE = “STABLE_BEAMS) N.B. These flags are NOT unique to each beam. |

## FULL LISTING OF SAFE_BEAM_FLAG THRESHOLDS

The Safe Beam Flag in LHC is based on a simple calculation involving the machine Energy and Intensity.  As of November 2007, the basic definition is as follows:

The Safe Beam Flag is True if:

Where Threshold is a fixed value of 1x1012 protons, this implies that:

- At injection energy (450GeV), a beam with intensity of 1 x 1012 protons will be considered SAFE, anything above this will be considered UNSAFE.

- At collision energy (7000GeV), a beam with intensity of ≈9.4 x 109 protons will be considered SAFE, anything above this will be considered UNSAFE.

The range of possible energies has been windowed, and the relevant intensities pre-calculated in order to facilitate the calculation of the Safe Beam Flag within FPGA architectures.

| Name | Lower Energy Value | Upper Energy Value | Intensity Value |
| --- | --- | --- | --- |
|  | [GeV] | [16-bit] [1 = 1.2x108] | [GeV] | [16-bit] [1 = 1.2x108] | [protons] | [24-bit] [1 = 1x108] |
|  | 0 | 0000 | 444.840 | 0E7B | Always FALSE | Always FALSE |
| SAFE_BEAM_FLAG_1 | 444.960 | 0E7C | 565.800 | 126B | 1.000E+12 | 002710 |
| SAFE_BEAM_FLAG_2 | 565.920 | 126C | 681.600 | 1630 | 6.774E+11 | 001A76 |
| SAFE_BEAM_FLAG_3 | 681.720 | 1631 | 797.520 | 19F6 | 4.936E+11 | 001347 |
| SAFE_BEAM_FLAG_4 | 797.640 | 19F7 | 913.320 | 1DBB | 3.780E+11 | 000EC3 |
| SAFE_BEAM_FLAG_5 | 913.440 | 1DBC | 1029.120 | 2180 | 3.002E+11 | 000BB9 |
| SAFE_BEAM_FLAG_6 | 1029.240 | 2181 | 1145.040 | 2546 | 2.450E+11 | 000992 |
| SAFE_BEAM_FLAG_7 | 1145.160 | 2547 | 1260.840 | 290B | 2.044E+11 | 0007FB |
| SAFE_BEAM_FLAG_8 | 1260.960 | 290C | 1376.760 | 2CD1 | 1.735E+11 | 0006C6 |
| SAFE_BEAM_FLAG_9 | 1376.880 | 2CD2 | 1492.560 | 3096 | 1.494E+11 | 0005D6 |
| SAFE_BEAM_FLAG_10 | 1492.680 | 3097 | 1608.360 | 345B | 1.302E+11 | 000516 |
| SAFE_BEAM_FLAG_11 | 1608.480 | 345C | 1724.280 | 3821 | 1.147E+11 | 00047A |
| SAFE_BEAM_FLAG_12 | 1724.400 | 3822 | 1840.080 | 3BE6 | 1.019E+11 | 0003FB |
| SAFE_BEAM_FLAG_13 | 1840.200 | 3BE7 | 1956.000 | 3FAC | 9.124E+10 | 000390 |
| SAFE_BEAM_FLAG_14 | 1956.120 | 3FAD | 2071.800 | 4371 | 8.225E+10 | 000336 |
| SAFE_BEAM_FLAG_15 | 2071.920 | 4372 | 2187.600 | 4736 | 7.458E+10 | 0002E9 |
| SAFE_BEAM_FLAG_16 | 2187.720 | 4737 | 2303.520 | 4AFC | 6.800E+10 | 0002A7 |
| SAFE_BEAM_FLAG_17 | 2303.640 | 4AFD | 2419.320 | 4EC1 | 6.229E+10 | 00026E |
| SAFE_BEAM_FLAG_18 | 2419.440 | 4EC2 | 2535.240 | 5287 | 5.730E+10 | 00023D |
| SAFE_BEAM_FLAG_19 | 2535.360 | 5288 | 2651.040 | 564C | 5.292E+10 | 000211 |
| SAFE_BEAM_FLAG_20 | 2651.160 | 564D | 2766.840 | 5A11 | 4.905E+10 | 0001EA |
| SAFE_BEAM_FLAG_21 | 2766.960 | 5A12 | 2882.760 | 5DD7 | 4.561E+10 | 0001C8 |
| SAFE_BEAM_FLAG_22 | 2882.880 | 5DD8 | 2998.560 | 619C | 4.254E+10 | 0001A9 |
| SAFE_BEAM_FLAG_23 | 2998.680 | 619D | 3114.360 | 6561 | 3.978E+10 | 00018D |
| SAFE_BEAM_FLAG_24 | 3114.480 | 6562 | 3230.280 | 6927 | 3.730E+10 | 000174 |
| SAFE_BEAM_FLAG_25 | 3230.400 | 6928 | 3346.080 | 6CEC | 3.505E+10 | 00015E |
| SAFE_BEAM_FLAG_26 | 3346.200 | 6CED | 3462.000 | 70B2 | 3.302E+10 | 00014A |
| SAFE_BEAM_FLAG_27 | 3462.120 | 70B3 | 3577.800 | 7477 | 3.116E+10 | 000137 |
| SAFE_BEAM_FLAG_28 | 3577.920 | 7478 | 3693.600 | 783C | 2.946E+10 | 000126 |
| SAFE_BEAM_FLAG_29 | 3693.720 | 783D | 3809.520 | 7C02 | 2.791E+10 | 000117 |
| SAFE_BEAM_FLAG_30 | 3809.640 | 7C03 | 3925.320 | 7FC7 | 2.648E+10 | 000108 |
| SAFE_BEAM_FLAG_31 | 3925.440 | 7FC8 | 4041.240 | 838D | 2.517E+10 | 0000FB |
| SAFE_BEAM_FLAG_32 | 4041.360 | 838E | 4157.040 | 8752 | 2.395E+10 | 0000EF |
| SAFE_BEAM_FLAG_33 | 4157.160 | 8753 | 4272.840 | 8B17 | 2.283E+10 | 0000E4 |
| SAFE_BEAM_FLAG_34 | 4272.960 | 8B18 | 4388.760 | 8EDD | 2.179E+10 | 0000D9 |
| SAFE_BEAM_FLAG_35 | 4388.880 | 8EDE | 4504.560 | 92A2 | 2.082E+10 | 0000D0 |
| SAFE_BEAM_FLAG_36 | 4504.680 | 92A3 | 4620.480 | 9668 | 1.992E+10 | 0000C7 |
| SAFE_BEAM_FLAG_37 | 4620.600 | 9669 | 4736.280 | 9A2D | 1.908E+10 | 0000BE |
| SAFE_BEAM_FLAG_38 | 4736.400 | 9A2E | 4852.080 | 9DF2 | 1.829E+10 | 0000B6 |
| SAFE_BEAM_FLAG_39 | 4852.200 | 9DF3 | 4968.000 | A1B8 | 1.755E+10 | 0000AF |
| SAFE_BEAM_FLAG_40 | 4968.120 | A1B9 | 5083.800 | A57D | 1.686E+10 | 0000A8 |
| SAFE_BEAM_FLAG_41 | 5083.920 | A57E | 5199.720 | A943 | 1.622E+10 | 0000A2 |
| SAFE_BEAM_FLAG_42 | 5199.840 | A944 | 5315.520 | AD08 | 1.561E+10 | 00009C |
| SAFE_BEAM_FLAG_43 | 5315.640 | AD09 | 5431.320 | B0CD | 1.503E+10 | 000096 |
| SAFE_BEAM_FLAG_44 | 5431.440 | B0CE | 5547.240 | B493 | 1.449E+10 | 000090 |
| SAFE_BEAM_FLAG_45 | 5547.360 | B494 | 5663.040 | B858 | 1.398E+10 | 00008B |
| SAFE_BEAM_FLAG_46 | 5663.160 | B859 | 5778.840 | BC1D | 1.350E+10 | 000086 |
| SAFE_BEAM_FLAG_47 | 5778.960 | BC1E | 5894.760 | BFE3 | 1.304E+10 | 000082 |
| SAFE_BEAM_FLAG_48 | 5894.880 | BFE4 | 6010.560 | C3A8 | 1.261E+10 | 00007E |
| SAFE_BEAM_FLAG_49 | 6010.680 | C3A9 | 6126.480 | C76E | 1.220E+10 | 000079 |
| SAFE_BEAM_FLAG_50 | 6126.600 | C76F | 6242.280 | CB33 | 1.181E+10 | 000076 |
| SAFE_BEAM_FLAG_51 | 6242.400 | CB34 | 6358.080 | CEF8 | 1.144E+10 | 000072 |
| SAFE_BEAM_FLAG_52 | 6358.200 | CEF9 | 6474.000 | D2BE | 1.109E+10 | 00006E |
| SAFE_BEAM_FLAG_53 | 6474.120 | D2BF | 6589.800 | D683 | 1.075E+10 | 00006B |
| SAFE_BEAM_FLAG_54 | 6589.920 | D684 | 6705.720 | DA49 | 1.043E+10 | 000068 |
| SAFE_BEAM_FLAG_55 | 6705.840 | DA4A | 6821.520 | DE0E | 1.013E+10 | 000065 |
| SAFE_BEAM_FLAG_56 | 6821.640 | DE0F | 6937.320 | E1D3 | 9.837E+09 | 000062 |
| SAFE_BEAM_FLAG_57 | 6937.440 | E1D4 | 7053.240 | E599 | 9.559E+09 | 00005F |
| SAFE_BEAM_FLAG_58 | 7053.360 | E59A | 7169.040 | E95E | 9.294E+09 | 00005C |
| SAFE_BEAM_FLAG_59 | 7169.160 | E95F | 7284.960 | ED24 | 9.040E+09 | 00005A |
| SAFE_BEAM_FLAG_60 | 7285.080 | ED25 | 7400.760 | F0E9 | 8.797E+09 | 000057 |
| SAFE_BEAM_FLAG_61 | 7400.880 | F0EA | 7516.560 | F4AE | 8.564E+09 | 000055 |
| SAFE_BEAM_FLAG_62 | 7516.680 | F4AF | 7632.480 | F874 | 8.341E+09 | 000053 |
| SAFE_BEAM_FLAG_63 | 7632.600 | F875 | 7748.280 | FC39 | 8.127E+09 | 000051 |
| SAFE_BEAM_FLAG_64 | 7748.400 | FC3A | 7864.200 | FFFF | 7.921E+09 | 00004F |

# FORCING and TUNING

It is possible to remotely tune the threshold of SPS PROBE BEAM (PROBE_BEAM_LIMIT), and to remotely force the Safe Beam Flags.

Note that this FORCING and TUNING must take into account that there will be two generators in the SPS SMP and two more in the LHC SMP.  Multiple values must be written.

## TUNING THE SPS PROBE BEAM FLAG

It is possible to adjust the value which is used for the calculation of the PROBE BEAM FLAG in the SPS Flag Generator.  The value written must be the beam intensity in 24-bits (1-bit = 1x108 charges) and must be less than the value for PROBE_BEAM_LIMIT.  Writing an invalid value will result in the value of PROBE_BEAM_LIMIT being used for the calculation.

## FORCING LHC Safe Beam Flag FALSE

The LHC Safe Beam Flags can be forced FALSE, by setting bits in the SMP Generators.  It will be possible to force any of the four Safe Beam Flags to FALSE independently of the other safe beam flags.

- SAFE BEAM FLAG 1 A

- SAFE BEAM FLAG 1 B

- SAFE BEAM FLAG 2 A

- SAFE BEAM FLAG 2 B

Details regarding the methods to force the flags will be made available in due course.