## Slide 1: Experience with BLMs
B. Dehning
CERN BE/BI

## Slide 2: Content
Specification
Concept
Hardware failures
System tests
  Firmware
  With beam (delays)
  Online (Sanity Check)
Post mortem data
Logging data

## Slide 3: Beam Loss Monitor Specification
5. USE OF THE BLM’S FOR MACHINE PROTECTION
The strategy for machine protection impacts on the BLM design in two ways, its time response and the reliability.
Protection of the machine from beam losses has two aspects:
• protection against beam losses that could lead to damage of equipment,
• protection against beam losses that could lead to a quench of a magnet.
Since a repair of superconducting magnets would take several weeks, the protection against damage has highest priority and damages should be strictly avoided (SIL 3, 1E-8 to 1E-7 1/h).
In case of a quench, the quench protection system would prevent equipment damage. However, the beam would be lost and re-establishing operation would take several hours. Therefore the number of quenches should be minimized.

## Slide 4
Beam Loss Measurement System Layouts
Ionisation chamber
  Function: observation and interlock
  3700 installed
  Over 90 % connected to interlock/dump system
Secondary emission detector
  Function: observation
  300 installed

## Slide 5: Quench and Damage Levels
Specifications
  Time resolution ½ turn, 40 us
  Average calculation loss:
    12 values, 40 us to 83 s
  Max amplitude 23 Gy/s
  Min amplitude
    1E-4 Gy/s @ 40 us
    3E-7 Gy/s @ 1.3 s
  Dynamic
    2E5 @ 40 us
    ~ 1E8 @ 1.3 s
  Damage level
    2000 Gy/s @ 1 ms
  All channels could be connected to the interlock system
  Thresholds
    Loss duration dependent, 12 values
    Energy dependent, 32 values
    About 1.5 E6 thresholds
450 GeV
3.5 TeV
5.0 TeV
7.0 TeV
Quadrupole and bending magnet thresholds

## Slide 6: BLM Online Display
LHC @ 450 GeV
Offset to check connectivity
ATLAS
ALICE

## Slide 7: System settings & data flow
Beam permit signal flow

## Slide 8: Overview of H/W Failures (since Feb. 2010)
9 IC with bad soldering
(out of 3700)
9 GOH with low power
1 damaged connector
out of 1500
7 CFC with ‘noisy’ components
2 cards with bad soldering out of 359
7 with ‘weak’ receivers
out of 1500
2 with failed SRAM out of 350
2 failed CPU RIO3
out of 25
1 VME Power Supply, out of 25
Number of failures regarded as manageable

## Slide 9: Functional Tests Overview PhD thesis G. Guaglio
Radioactive source test
Functional tests before installation
Barcode check
HV modulation test
Double optical line comparison
Offset to check connectivity (10 pA test)
System component identity check
Beam inhibit lines tests
Detector
Tunnel electronics
Surface electronics
Combiner
Inspection frequency:
Reception Installation and yearly maintenance Before (each) fill Parallel with beam
Current source test
Threshold table data base comparison

## Slide 10: System Verification Tests Surface Electronics Firmware Tests
Automatic on Vertical Slice Test system (before releasing new firmware)
Using front-end electronics emulator
  Lab tests
    Exhaustive Threshold triggering tests [also in LHC done]
    Optical Link Reception and Status tests
    Linearity, impulse, and some predefined patterns of input signals check
  Beam tests
    injected low intensity beams (pilot), debunched them and dumped with the operator switch.
    closed one of the collimator jaw of a TCP at point 3 and injected 3 times pilot beam 1.

## Slide 11: System Verification Tests Surface Electronics Firmware Tests
Automatic on Vertical Slice Test system (before releasing new firmware)
Using front-end electronics emulator
  Lab tests
    Exhaustive Threshold triggering tests [also in LHC]
    Optical Link Reception and Status tests
    Linearity, impulse, and some predefined patterns of input signals check
  Beam tests
    injected low intensity beams (pilot), debunched them and dumped with the operator switch.
    closed one of the collimator jaw of a TCP at point 3 and injected 3 times pilot beam 1.
Detector with filter, B. Holzer

## Slide 12: System latency (2009 – 02/2010)
Analysed several Beam Dumps in detail.
Difference in time between the bunch at injection kicker magnet and the break of the beam permit loop (by the BLMS) recorded at the BIC was always between 100 and 130 μs.
Time of flight:
  MKI => monitor = 10 μs
  monitor => acq. electronics (0.5 km cable) = 3 μs
  Acq. => processing electronics (1 km fibre) = 3 μs
Detection of change in frequency in the daisy-chain = 5 μs
Integration in the acquisition electronics = 40 μs.
Decision at the BLETC (for fast losses) is taken every 40 μs.
Processing of data to decide < 1 μs.

## Slide 13: System Tests == Sanity Checks
Initiative - own ideas, responsibility & autonomous work
Beam loss monitors in the tunnel
Modulated High Voltage
BLM acquisition chain
Digital signal processing and decision inside the FPGA
BLECS
BLM Diagnostic application
Normal behavior
Capacitor missing or disconnected
Samples ( from 1Hz logging => 15Hz )
Amplitude [RS09_Bit]
Decision of pass or fail in surface electronics FPGA (combiner)
Every 24 h required, (beam permit inhibit if time limit exceeded
Tests
  Comparison between data base and backend electronics (MCS)
  Internal beam permit line test (VME crate)
  Connectivity check (modulation of chamber HV voltage supply amplitude an phase limit checks
  Duration of test: about 7 minutes

## Slide 14: Post Mortem Data (some examples)
PM application: BLM data of 0.082 sec
online available
Longer PM buffer: BLM data of 1.72 sec
offine available
43000 values (40 us)
2000 values (40 us)
Loss in a bending magnet
Monitors
Time

## Slide 15: Post Mortem Data (some examples), Zoom
Loss from primary event
+
dump system loss

## Slide 16: Post Mortem Losses in Dump Line and Dump, Secondary Emmission Monitors

## Slide 17: Logging Data Base Data (fast event)
Beam 1 loss (from left to right)
Loss monitor of B1 at MQ 15 over threshold
Beam 2 monitors measure about 5 times lower loss
Shown average value over 2.5 ms (maximum in 1.3 s)

## Slide 18: Threshold and Loss Data versus Averaging Duration
Online Display and Logging data base Storage
Data reduction in surface electronics
  Averages from 40 us to 660 ms == every 1.3 second max value in last 1.3 s
  Average 1.3 s directly stored
  Average 83 s every minute
  Logging 40 GByte / day
Reconstruction of duration of events possible by max value shapes (identification of kink)

## Slide 19: BLM System Upgrades
Online program predicting loss characteristics and likely loss origin, PhD
Long cable issue in IP3
Development of an Detector with intermediate measurement range
New cables for noise channels (7 TeV operation)
Data set: 8.1.2010-15.1.2010
Ratio new / standart proto type 8, aim 100

## Slide 20: Summary
No evidence has been found that a single beam loss event has been missed
  The initial threshold settings have to be sufficiently conservative in order not to damage the LHC magnets. During the initial runs of the LHC, they must then be iteratively adjusted. (Audit report 2008)
The hardware failures never caused a degradation of the reliability of the system
False dumps
  The number of hardware failures are as expected (reliability and safety study, PhD. G. Guaglio)
  No noise events

## Slide 21: Spare Slides

## Slide 22: Gain Variation of SPS Chambers
30 years of operation
Measurements done with installed electronic
Relative accuracy
  Ds/s < 0.01 (for ring BLMs)
  Ds/s < 0.05 (for Extr., inj. BLMs)
Gain variation only observed in high radiation areas
Consequences for LHC:
  No gain variation expected in the straight section and ARC of LHC
  Variation of gain in collimation possible for ionisation chambers
Test with Cs137
Total received dose:
  ring 0.1 to 1 kGy/year
  extr 0.1 to 10 MGy/year

## Slide 23: Thresholds Test with 3 corrector orbit bump measurements
3 corrector bump already used during threshold tests
Top: BLM signal at trigger level vs dcum
Bottom: BLM signal vs bump size
Beam position reproducibility is estimated to 150 μm peak to peak, max BLM signal variation 50 %

## Slide 24: Fault Tree Analysis
AND Gate
EVENT
1
EVENT
2
AND Gate
EVENT
1
EVENT
2
The probability to have an Failure Mode A, Pr{A}, is calculated per each Failure Modes of the FMECA, given the hazard rate, the repair rate and the inspection period .
OR Gate
EVENT
1
EVENT
2
OR Gate
EVENT
1
EVENT
2
Damage
Risk
Blind
FEE
Blind
BEE
False Alarm
by
transmission
Optical
line
1
Optical
line
2
Almost 160 Failure Modes have been defined for the BLMS using the FMD-97 standard.
Three Ends Effects:
1. Damage Risk: probability not to be ready in case of dangerous loss.
2. False Alarm: probability to generate a false alarm.
3. Warning: probability to generate a maintenance request following a failure of a redundant component.

## Slide 25: Fault Trees Results
The probabilities to fail (unavailability) for the BLMS have been calculated.
Per each End Effects, the major contributors to such probabilities have been pointed out too.
 | Consequences per year | Weakest components | Notes
Damage Risk | 5·10-4 (100 dangerous losses) | Detector (88%) Analogue electronics (11%) | Detector likely overestimated (60% CL of no failure after 1.5 106 h).
False Alarm | 13 ± 4 | Tunnel power supplies (57%) VME fans (28%) | Tunnel power supplies likely underestimated (see sensitivity example).
Warning | 35 ± 6 | Optical line (98%) VME PS ( 1%) | LASER hazard rate likely overestimated by MIL.