## Slide 1: Reliability tests of the lhc beam loss monitoring fpga firmware
Csaba F. Hajdu
09/04/2010

## Slide 2: Outline
Introduction
  The LHC Beam Loss Monitoring system
  The Threshold Comparator firmware
  Verification: Motivation
Verification methodology
  Simulation
  Hardware-based testing
  Software-based testing
Procedure for new release
Conclusion

## Slide 3: 1/1. Introduction The LHC Beam Loss Monitoring system
The LHC Beam Loss Monitoring system
  One of the most critical protection systems
    Protects magnets from quenches, collider from damage
    Provides data for diagnostics and machine tuning
  Nearly 4’000 monitors
    Ionization Chambers (IC), Secondary Emission Monitors (SEM)
  Data acquisition: Current to Frequency Converter (CFC)
  Data processing: Threshold Comparator (TC)
      FPGA-based
    Calculation of integrals over different time windows
    Beam abort trigger when necessary

## Slide 4: 1/2. Introduction The Threshold Comparator firmware

## Slide 5: 1/3. Introduction Verification: Motivation
Verification of the Threshold Comparator firmware
  Verification: about 70% of the design cycle (Doulos)
Sequential digital design of great complexity
  Exhaustive verification impractical
  Comprehensive verification environment
    Different approaches of verification targeting different aspects of design
      Functional simulation
      Hardware-based approach
      Software-based approach

## Slide 6: 2/1. Simulation Scope

## Slide 7: 2/2. Simulation The RCC block
The RCC block
  Receives the redundant input signals from TLKs
  Checks packets for errors
    CRC, Card ID, Frame ID, link unavailable
    Can issue beam abort triggers as required
  Decides which packet to use for further processing

## Slide 8: 2/3. Simulation Description
Functional simulation
  Verify compliance to functional requirements of spec
Testbench (ModelSim)
  “Black box” design methodology
    Based only on specification
  Stimulus read from file
  Automatic checking of outputs
    Comparison of versions
      Regression testing
      Detection of new bugs

## Slide 9: 2/4. Simulation Sample output waveforms
Time
I/O signals
Output waveform for optical inspection

## Slide 10: 2/5. Simulation Sample output waveforms
Frame transmission
Strobe and error signals
Time
I/O signals

## Slide 11: 2/6. Simulation Automatic output checker – Description
Automatic output checker
  Checks the output of the block vs. the expected output based on stimulus from file
  Complements visual inspection
Code snippet of the automatic output checker

## Slide 12: 2/7. Simulation Automatic output checker – Sample outputs
Error-free output
Output with errors

## Slide 13: 3/1. Hardware-based check Scope

## Slide 14: 3/2. Hardware-based check Motivation
In situ test of the TC in VME crate
  Emulation of output signals of CFC
TC architecture
  BI standard DAB64x card
  Optical receiver mezzanine
    4 TLKs, signal from 2 CFCs
  FPGA processing firmware

## Slide 15: 3/3. Hardware-based check The “Vertical Slice” card
New mezzanine for DAB64x card
  Two standard Gigabit Optical Hybrid transmitters
    Emulation of one CFC; more with optical splitters
Custom FPGA firmware

## Slide 16: 3/4. Hardware-based check Installation

## Slide 17: 3/5. Hardware-based check Features
Arbitrary Tx data
  Comparison of different TC firmware versions
  Playback of LHC capture data for analysis
Tx errors
  CRC, CID, FID
Wrong configuration
Errors in physical layer
Manual testing procedure
  Results read out in Expert application

## Slide 18: 3/6. Hardware-based check Features – Playback of capture data
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
 | 0 | 1 | 11967 | 7378 | 3720 | 1472 | 518 | 216 | 70 | 34 | 14 | 7 | 9 | 4 | 7 | 9 | 8 | 9 | 10 | 8 | 11 | 7 | 8 | 11 | 6 | 9 | 9 | 5 | 9 | 5
INPUT
OUTPUT
Samples from an IC in LHC tunnel: loss of a single bunch (40us)
12 Running Sums (integrals)

## Slide 19: 4/1. Software-based check Scope

## Slide 20: 4/2. Software-based check Description
Exhaustive verification of the behavior of the Threshold Comparator block
  Every threshold value has to trigger one by one
    16 cards/crate
    16 detectors/TC card
    12 integration windows/detector
    32 beam energy levels
      98’304 testcases/crate
VME readout check
  The same testcase repeated 500’000 times

## Slide 21: 4/3. Software-based check The “Exhaustive Threshold Triggering”
VME crates
  “Front End Computer” (FEC)
  Combiner (CS)
Algorithm running on FEC
  Loads threshold maps causing one chosen threshold to trigger a beam abort
  Checks the result on TC and CS

## Slide 22: 4/4. Software-based check Algorithm

## Slide 23: 5. New release
Procedure
  A few hours of manual testing
    Carry out simulation with testbench
        If RCC block has been modified
    Perform hardware-based test
      CRC errors
      CID errors
      FID errors
      Lost frames
  24 hours of automatic testing
    Execute the software-based “Exhaustive testing”
All tests need to pass!
Inspection of the code changes by the verification engineer
  Independent review

## Slide 24: 6. Conclusion
Numerous bugs identified and fixed
Number of bugs found vs. time converging
  Reason for optimism
No bugs found during operation
  Sheer good luck?