MRV Communications, Inc.

MARVEL SERIES 8

RECEIVER

THE Source for your Source

FEATURES

- Long  Wavelength	- Low power consumption

- Low Pulse Width Distortion	- Standard 5V Power Supply

- High Responsivity	- 8 Pin, ST, FC, SC Connectorized or Pigtailed

- High Speed	- Singlemode and Multimode Applications

RECEIVER CHARACTERISTICS ( T= 25°C )

| Parameter | Symbol | Minimum | Typical | Maximum | Unit |
| --- | --- | --- | --- | --- | --- |
| Wavelength |  | 1200 |  | 1550 | nm |
| Responsivity (Single-ended) | R | 5.0 |  |  | mV/µW |
| Responsivity (Differential) | R | 10.0 |  |  | mV/µW |
| Supply Current | Icc |  | 26 | 32 | mA |
| Data Rate |  |  |  | 125 | Mhz |
| Input Power ( Average ) |  |  |  | 60 | W |
| RMS Output Spectral Density Noise Voltage |  |  | 27 |  | nV/Hz |
| Rise/Fall Time | Tr,Tf |  | 2.4,2.9 |  | ns |
| Output Bias Voltage |  |  | 3.3 | 3.7 | V |
| Output Offset Voltage |  |  |  | 80 | mV |
| Output Sink/ Source Current |  | 3 | 4 |  | mA |
| Output Resistance (single-ended) |  | 7 | 15 | 21 |  |
| Output Resistance (Differential) |  | 14 | 30 | 42 |  |
| Power Supply Rejection Ratio |  | 26 | 33 |  | dB |
| Maximum Differential Output Voltage Swing |  |  |  | 1.4 | V p-p |

ABSOLUTE MAXIMUM RATINGS

| PARAMETER | SYMBOL | RATING | UNIT |
| --- | --- | --- | --- |
| Supply Voltage | Vcc | 6 | VOLTS |
| Operating Temp | Top | 0 - 70 | °C |
| Storage Temp | Tstg | -40 - 85 | °C |

Ordering Information

MRR   XX  - 125 - 8X

Receiver	Pinout Option (1-5)

Connector*

* 	ST=Singlemode St, MT=Multimode ST, FC=Singlemode FC, MC=Multimode FC,

SP=Singlemode Pigtail, MP=Multimode Pigtail, SC=Singlemode SC, MS=Multimode SC

Package Style “ST”-A

Package Style “ST”-B

Package Style “FC”

Package Style “SP”

Package Style “SC”/ “MSC”

Board Diagram

Pinout Diagram

Options

# Text boxes

RX-8.DOC 3/18/98