MRV Communications, Inc.

LED SERIES 1

PIGTAILED MINI-HOUSING

THE Source for your Source

FEATURES

- 1300/1550 NM  Wavelength	- High Speed

- High Optical Power	- Low Modal Noise

- Low Operating Current	- Pigtailed Mini-Housing

- High Operating Temperature	- For Singlemode & Multimode Use

CHARACTERISTICS ( T= 25°C )

| Parameter | Sym | Condition | Min | Typical | Max | Unit |
| --- | --- | --- | --- | --- | --- | --- |
| Wavelength | p | CW | 1260 | 1310 | 1340 | nm |
| Spectral Width |  | CW(FWHM) | 30 |  | 70 | nm |
| Operating Current | Iop | CW |  | 80 | 100 | mA |
| Output Power | Po | CW | See Below SM(9/125),MM(50/125) |  |
| Wavelength | p | CW | 1510 | 1550 | 1580 | nm |
| Spectral Width |  | CW(FWHM) | 45 |  | 100 | nm |
| Operating Current | Iop | CW |  | 80 | 100 | mA |
| Output Power | Po | CW | See Below SM(9/125),MM(50/125) |  |
| Rise Time/Fall Time | Tr/Tf |  |  | 1.5,2.5 |  | ns |
| Forward Voltage | Vf |  |  | 1.2 | 1.7 | V |

OUTPUT POWER ( T= 25°C )

| Part Number 1300 nm Singlemode | Min | Typ | Unit | Part Number 1300 nm Multimode | Min | Typ | Unit |
| --- | --- | --- | --- | --- | --- | --- | --- |
| MREDSP/SPF001-1 | 10 | 20 | W | MREDMP/MPF005-1 | 50 | 75 | W |
| MREDSP/SPF003-1 | 30 | 45 | W | MREDMP/MPF007-1 | 70 | 100 | W |
| MREDSP/SPF005-1 | 50 | 75 | W | MREDMP/MPF010-1 | 100 | 150 | W |
| MREDSP/SPF010-1 | 100 | 150 | W | MREDMP/MPF015-1 | 150 | 200 | W |
| MREDSP/SPF013-1 | 130 | 175 | W | MREDMP/MPF020-1 | 200 | 300 | W |
| MREDSP/SPF015-1 | 150 | 200 | W |  |  |  |  |

OUTPUT POWER ( T= 25°C )

| Part Number 1550 nm Singlemode | Min | Typ | Unit | Part Number 1550 nm Multimode | Min | Typ | Unit |
| --- | --- | --- | --- | --- | --- | --- | --- |
| MREDSP/SPF5001-1 | 10 | 20 | W | MREDMP/MPF5003-1 | 30 | 40 | W |
| MREDSP/SPF5002-1 | 20 | 30 | W | MREDMP/MPF5005-1 | 50 | 75 | W |
| MREDSP/SPF5003-1 | 30 | 40 | W | MREDMP/MPF5007-1 | 70 | 100 | W |

ABSOLUTE MAXIMUM RATINGS

| PARAMETER | SYMBOL | CONDITIONS | RATING | UNIT |
| --- | --- | --- | --- | --- |
| LED reverse Voltage | VrLED | CW | 2.5 | VOLTS |
| Operating Temp | Top |  | -20 to +60 | °C |
| Storage Temp | Tstg |  | -30 to +80 | °C |

Package Style “SP”

Package Style “SPF”

Pinout - 3 Pin

# Text boxes

LEDSP.DOC 2/4/99