## Slide 1: Proposal on Threshold Corrections for RC Filters
Eva Barbara Holzer
for the BLM team
LHC MPP
CERN, July 17, 2010

## Slide 4: History (April 2010): Injection of higher intensity
RC filter for the monitors requested by the injection team factor 25 (all are external monitors;)
Maximum current will be reduced by a factor of 8.3 by RC filter and additional factor of 3 with (future) thresholds
Factor of ~10 between signal on external and internal monitors
For moment the threshold values not changed!
For all other energies the thresholds are now too high
  A quench could occur
  New thresholds to be calculated asap
All these monitors set to maskable
Estimate: Quench of magnet by outside shower if injection intensity 2e13

## Slide 5: New Thresholds after filter installation
Allow injection losses
   450 GeV thresholds have to be adapted to the shape of instantaneous (delta) losses.
  Well defined procedure, which was already done for different magnets (not discussed here).
All other energies: adapt thresholds to ‘cancel’ the effect of the filter
  Definition of cancel: same amount of loss leads to beam abort with the same time delay
  Correction factor for thresholds depends on the time evolution of the beam loss
  100% correction for all possible loss scenarios is not possible
   need to decide on a reasonable loss evolution

## Slide 6: Investigate Dependence on Loss Evolution
Filter response approximated by exponentially decaying signal (rise time = zero).
    For bigger filters (rise time 0.3ms) this is not a good approximation
    For the filter in question the rise time is between 0.12 ms to 0.2ms (to be confirmed). If confirmed, the thresholds of the first 3 integration times should be reduced further accordingly.
Analytical calculation
  Filter response folded with loss evolution
  Integrated signal

## Slide 7: Proton loss distributions
Time normalized to integration time
Protons lost in a.u.
δ(t - 0)
δ(t - integration_time)

## Slide 8: Loss distributions: correction effect gets stronger
δ(t - 0)
  1-exp(-RS/RC) RS…integration time RC…filter time constant
Constant loss 1-(RC/RS)*(1-exp(-RS/RC))
Linear increasing loss
  1+(2*RC*RC/(RS*RS))*(1-exp(-RS/RC))-2*RC/RS
Exponentially increasing with time constant equal to integration time:
  The longer the running sum, the slower the development of the loss to protect against
  Argument: The running sum RS5 with an integration time of 2.56 ms should protect against losses which develop on that time scale.
  The shortest RS has to protect against instantaneous (which are the most dangerous ones for the magnet).
δ(t - integration_time)
  not possible to cancel the effect (thresholds go towards zero when delta function approaches the end of the integration window)
  When corrections are calculated with δ(t - 0) the maximum time delay of the abort signal is the integration time of the RS

## Slide 9: Correction factors for RC time constant of 2ms
Multiplication correction factor for the 12 integration time windows. A factor of 1 means no correction.
Time [s]

## Slide 10: Correction factors for RC time constant of 2ms
 | RS [ms] | delta(t-0) 1-exp(-RS/RC) | const | linear | linear | Exp. | Delta/exp.
RS1 | 0.04 | 0.019801 | 0.009934 | 0.006633 | 0.006633 | 0.00604925 | 3.27335
RS2 | 0.08 | 0.039211 | 0.019736 | 0.013201 | 0.013201 | 0.01204168 | 3.256236
RS3 | 0.32 | 0.147856 | 0.075899 | 0.051266 | 0.051266 | 0.0468388 | 3.156704
RS4 | 0.64 | 0.273851 | 0.144216 | 0.098652 | 0.098652 | 0.09031911 | 3.032038
RS5 | 2.56 | 0.721963 | 0.435967 | 0.318802 | 0.318802 | 0.29519402 | 2.445723
RS6 | 10.24 | 0.994024 | 0.805855 | 0.685213 | 0.685213 | 0.65328106 | 1.521587
RS7 | 81.92 | 1 | 0.975586 | 0.952364 | 0.952364 | 0.94379834 | 1.059548
RS8 | 655.36 | 1 | 0.996948 | 0.993915 | 0.993915 | 0.99273469 | 1.007318
RS9 | 1310.72 | 1 | 0.998474 | 0.996953 | 0.996953 | 0.99635857 | 1.003655
RS10 | 5242.88 | 1 | 0.999619 | 0.999237 | 0.999237 | 0.99908799 | 1.000913
RS11 | 20971.52 | 1 | 0.999905 | 0.999809 | 0.999809 | 0.9997719 | 1.000228
RS12 | 83886.08 | 1 | 0.999976 | 0.999952 | 0.999952 | 0.99994297 | 1.000057

## Slide 11: Conclusion for RC time constant of 2ms
Maximum difference
  between δ(t - 0) and the exponential increase
  factor 3.3
Proposal
  Apply the least correction: δ(t - 0)
    Practical reasons
      RS5 is comparatively low already
      This type of correction is already applied on all RS1 – RS3 for ion signal effect (ionization chamber does not give delta signal)
    Biggest difference seen is only factor 3.3
Do we need to protect against faster losses?
Rise time effect (measured: 0.12 ms to 0.2ms) ?

## Slide 12: Some more slides

## Slide 13: Over-injection

## Slide 14: Over-injection
Thresholds 4 MBX monitors now allow for over-injection onto a ‘fat’ pilot. Requested: Brennan
    40us to 10ms (RS1 to RS6 ) changed for 450 GeV
  BLMEI.04R8.B2E10_MBXB and BLMEI.04L2.B1E10_MBXA
    Up to ‘pilot’ of ~8e9
    At the next possibility: increase margin to 1.2e10 (same as MQXA)
    Thresholds to be recalculated (unnecessarily low for higher energies)
  BLMEI.04R8.B2E20_MBXB and BLMEI.04L2.B1E20_MBXA
    Final – to be verified
Threshold on TCT not increased (requested: Ralph)  next in the line to trigger
Two additional corrections:
  Swap names: BLMEI.04L2.B1E10_MBXA and BLMEI.04L2.B1E20_MBXA
    Past logging data reassigned accordingly – should be transparent
  Corrected threshold settings (3 MBX monitors were in wrong family)
ECR to be done once all changes finalized